# Base class “NeuroTool”
(all fields new to N toolbox)
## Summary of Methods:

Method Name	Description
calcpsthbins	calculates bins based on psthbinsize and stores in UnitData

## Summary of Fields:

Variable Name	Variable Description	Variable Type
D	description in following tables
psthbinsize	bin size in seconds for D.UnitData.psthbins	double

# N.defaults
## Summary of Fields (user changeable):

Variable Name	Variable Description	Variable Type
psthbinsize	default binsize	double
psthbsexpected	expected binsize range(warn happens outside range)	[low, high] double

## Summary of Methods:

Method Name	Description
N.defaults	returns all defaults stored in file NTdefaults.mat
N.defaults(var)	returns default for field, ‘var’
N.defaults(var, val)	assigns new value, ‘val’ to field ‘var’ and saves in NTdefaults.mat

# All following structures are elements of “D” in the root class variable
# Stimulus Structure
## Summary of Fields:

Variable Name	Variable Description	Variable Type
AmplitudeL	L pk-pk amplitude (V)	[Nreps x 1 double]
AmplitudeR	R pk-pk amplitude (V)	[Nreps x 1 double]
AttenuationL	L attenuation (dB)	[Nreps x 1 double]
AttenuationR	R attenuation (dB)	[Nreps x 1 double]
BBNlowerFreqL	L noise lower frequency limit (Hz)	[Nreps x 1 double]
BBNlowerFreqR	R noise lower frequency limit (Hz)	[Nreps x 1 double]
BBNupperFreqL	L noise upper frequency limit (Hz)	[Nreps x 1 double]
BBNupperFreqR	R noise upper frequency limit (Hz)	[Nreps x 1 double]
Channel	Output channel (‘L’, ‘R’, ‘BOTH’}	char
FirstTimestamp	Time of first instance for this stimulus (sec)	double
FixedDelayL	L delay time for all signals (sec)	[Nreps x 1 double]
FixedDelayR	R delay time for all signals (sec)	[Nreps x 1 double]
HoldTimeL	L duration between onset/offset ramps (sec)	[Nreps x 1 double]
HoldTimeR	R duration between onset/offset ramps (sec)	[Nreps x 1 double]
Indices	Location(s) of stimulus presentation	[Nreps x 1 double]
LAttenIndices	Locations(s) for each of the LAttenVals	{}
LAttenVals	Unique L attenuation values, sorted (dB)	[]
Nreps	# of repetitions of this stimulus	double
OutputFilename	Path to which original raw data were written	[char]
OutputTimeWithDelayL	L time of signal onset + delay (sec)	[Nreps x 1 double]
OutputTimeWithDelayR	R time of signal onset + delay (sec)	[Nreps x 1 double]
OutputTimestampL	L time of signal onset (stim. timestamp) (sec)	[Nreps x 1 double]
OutputTimestampR	R time of signal onset (stim. timestamp) (sec)	[Nreps x 1 double]
PA5idL	Id # for L PA5 attenuator	[Nreps x 1 double]
PA5idR	Id # for R PA5 attenuator	[Nreps x 1 double]
PhaseDegL	L tone phase (degrees)	[Nreps x 1 double]
PhaseDegR	R tone phase (degrees)	[Nreps x 1 double]
RAttenIndices	Locations for each of the RAttenVals	{[Nreps x 1 double]}
RAttenVals	Unique R attenuation values, sorted (dB)	[Natt vals X 1 dbl]
RampDownL	L signal offset time (sec)	[Nreps x 1 double]
RampDownR	R signal offset time (sec)	[Nreps x 1 double]
RampUpL	L signal onset time (sec)	[Nreps x 1 double]
RampUpR	R signal onset time (sec)	[Nreps x 1 double]
Spiketimes	Spiketimes for all cells, all sweeps (sec)	{Nunits x Nreps cell}
Spiketimes_PostStim	Spiketimes for next stimulus (sec)	{Nunits x Nreps cell}
Spiketimes_PreStim	Spiketimes for prior stimulus (sec)	{Nunits x Nreps cell}
psthbins	Spike count per psthbinsize (from Spiketimes)	{Nunits x Nreps cell}
psthwindows	Windows calculated with width	{Nunits x Nreps cell}
Sweepend	Time for end of sweep (sec)	[Nreps x 1 double]
Sweepstart	Time for start of sweep (sec)	[Nreps x 1 double]
Tagstring	Text tags for the marker for this stimulus type	[char]
TimeShiftL	Stimulus-specific delay for L channel (sec)	[Nreps x 1 double]
TimeShiftR	Stimulus-specific delay for R channel (sec)	[Nreps x 1 double]
Timestamp	Vector of timestamps for stimulus sweeps (sec)	[Nreps X 1 double]
ToneFreqL	L channel tone frequency (tone stim only) (Hz)	[Nreps x 1 double]
ToneFreqR	R channel tone frequency (Tone stim only) (Hz)	[Nreps x 1 double]
Type	'NOISE' 'WAVFILE' 'TONE' ‘NO_SOUND' 'BACKGROUND' 'UNKNOWN'	{char}
Var	Var structure	[1x2 struct]
WavFilenameL	.wav file played from L channel (wav stim only)	[char]
WavFilenameR	.wav file played from R channel (wav stim only)	[char]
id	DataWave ID code (?)	[Nreps x 1 double]
psthbinsum	spike count per time increment of size psthbinsize	[1 x # nonempty bins double]
psthbins	left bound timestamp for nonempty bins	[1 x # nonempty bins double]

# Var Structure

## Summary of Fields:

Variable Name	Variable Description	Variable Type

# Data Structure

## Summary of Fields:

Variable Name	Variable Description	Variable Type
Info	Info structure	Struct
Marker	Marker structure	Struct
MarkerTimes	Vector of Marker timestamps (sec)	[1 X Nmarkers double]
Probe	Struct array of Probe structure for spikes	[1 X Nprobes struct]
UnitData	Struct array of UnitData structures. Contains information about sorted (or unsorted) units	[1 X Nunits struct]

# Info Structure

## Summary of Fields:

Variable Name	Variable Description	Variable Type
MarkerCols	# of marker text columns in DataWave .txt file	1
MarkerTags	Marker tags from DataWave file	{NmarkerCols x 1}
NMarkerCols	# of marker columns	33
NSpikeCols	# of spike columns	4
NUnitCols	# of unit columns	4
Ncols	# of columns in DataWave .txt file	45
Ndatalines	# of lines with data in .txt file	21800
Nlines	Total # of lines in .txt file	21801
Nunits	Total # of units (includes junk, garbage, etc.)	11
SpikeCols	Columns in data file that contain spike data	[NSpikeCols X 1]
UnitCols	Columns that contain unit data	[NUnitCols X 1]
data1	Parsed text array of 1st line of data	{NCols x 1 char}
file	DataWave .txt file name	[char]
filename	DataWave .txt file path and name	[char]
header	Header structure	struct
path	path to DataWave .txt file	[char]

# header Structure (usually element in Info struct)

## Summary of Fields:

Variable Name	Variable Description	Variable Type
line	text of DataWave .txt file header line	{char}
fields	Field headers from DataWave .txt file	{nfields x 1 char}
nfields	# of header fields	double

# Marker Structure
This is a master list of the marker “tags” that are read in from the DataWave .txt output file.
## Summary of Fields:

Variable Name	Variable Description	Variable Type
AmplitudeL	L channel output signal peak-peak amplitude (mV)	[Nmarkers x 1 double]
AmplitudeR	R channel output signal peak-peak amplitude (mV)	[Nmarkers x 1 double]
AttenuationL	L PA5 attenuation (dB)	[Nmarkers x 1 double]
AttenuationR	R PA5 attenuation (dB)	[Nmarkers x 1 double]
BBNlowerFreqL	Broadband Noise, lower freq limit (Hz)	[Nmarkers x 1 double]
BBNlowerFreqR	Broadband Noise, lower freq limit (Hz)	[Nmarkers x 1 double]
BBNupperFreqL	Broadband Noise, upper freq limit (Hz)	[Nmarkers x 1 double]
BBNupperFreqR	Broadband Noise, upper freq limit (Hz)	[Nmarkers x 1 double]
FixedDelayL	delay time for all signals, all channels (sec)	[Nmarkers x 1 double]
FixedDelayR	delay time for all signals, all channels (sec)	[Nmarkers x 1 double]
HoldTimeL	duration of signal between ramps (sec)	[Nmarkers x 1 double]
HoldTimeR	duration of signal between ramps (sec)	[Nmarkers x 1 double]
M	raw marker data (text)	[1 x Nmarkers struct]
Nmarkers	Total number of markers (# stimuli + 1)	double
OutputFilename	DataWave .ddf filename	{Nmarkers x 1 cell}
OutputTimeWithDelayL	Time of signal + delay (sec)	[Nmarkers x 1 double]
OutputTimeWithDelayR	Time of signal + delay (sec)	[Nmarkers x 1 double]
OutputTimestampL	Time of signal start (sec)	[Nmarkers x 1 double]
OutputTimestampR	Time of signal start (sec)	[Nmarkers x 1 double]
PA5idL	id # for PA5 attenuator (0 = Right 1 = Left)	[Nmarkers x 1 double]
PA5idR	id # for PA5 attenuator (0 = Right 1 = Left)	[Nmarkers x 1 double]
PhaseDegL	L Tone phase (Degrees)	[Nmarkers x 1 double]
PhaseDegR	R Tone phase (Degrees)	[Nmarkers x 1 double]
RampDownL	L signal offset ramp time (sec)	[Nmarkers x 1 double]
RampDownR	R signal offset ramp time (sec)	[Nmarkers x 1 double]
RampUpL	L signal onset ramp time (sec)	[Nmarkers x 1 double]
RampUpR	R signal onset ramp time (sec)	[Nmarkers x 1 double]
StimulusTypeL		{Nmarkers x 1 cell}
StimulusTypeR		{Nmarkers x 1 cell}
TimeShiftL	L Stimulus-specific delay for stimulus (sec)	[Nmarkers x 1 double]
TimeShiftR	R Stimulus-specific delay for stimulus (sec)	[Nmarkers x 1 double]
Timestamp		{Nmarkers x 1 cell}
ToneFreqL	L Tone frequency (Hz)	[Nmarkers x 1 double]
ToneFreqR	R Tone frequency (Hz)	[Nmarkers x 1 double]
WavFilenameL	L output .wav file name (with drive:\path)	{Nmarkers x 1 cell}
WavFilenameR	R output .wav file name (with drive:\path)	{Nmarkers x 1 cell}
id	???	[Nmarkers x 1 double]
string	'NOISE' 'WAVFILE' 'TONE' ‘NO_SOUND' 'BACKGROUND' 'UNKNOWN'	[Nmarkers x 1 cell}
wavFilesL	unique L output .wav file names	[# x 1 struct]
wavFilesR	unique R output .wav file names	[# x 1 struct]

# M Structure (usually in Marker struct)

## Summary of Fields:

Variable Name	Variable Description	Variable Type
t	timestamp (sec)	double
string	text values of Marker information	{# marker fields x 1}

# wavFiles(L/R) Structure

## Summary of Fields:

Variable Name	Variable Description	Variable Type
uniqueNames	unique .wav file name	[1 X N double]
uniqueIndices	indices (in master, Marker indices) of the unique stimuli	double
Nunique	# unique filenames	double

# Probe Structure

## Summary of Fields:

Variable Name	Variable Description	Variable Type
cluster	cluster ID values (id number 0-nclusters, 0 corresponds to “junk” category)	[1 X N double]
nclusters	# of clusters for this probe (from Plexon)	double
t	timestamps for each spike (sec)	[1 X N double]

# MarkerTimes Array
[1 X Nmarkers] array of marker timestamps (in microseconds)
# UnitData Structure array
[1 X # of units] struct array, containing information about spike timestamps, organized
by unit # (units from probe 1 are first, then probe 2, etc.)
## Summary of Fields:

Variable Name	Variable Description	Variable Type
indices	indices into Probe structure arrays	[1 x # spikes double]
probe	electrode/tetrode number	double
sorted	0 if unsorted, 1 if sorted	double
timestamp	vector of timestamps for each spike	[1 x # spikes double]
unit	unit id value (0 = unsorted/junk, 1…n)	double
psthbinsum	spike count per time increment of size psthbinsize	[1 x # nonempty bins double]
psthbins	left bound timestamp for nonempty bins	[1 x # nonempty bins double]